## Slide 1
Integrating LoRaWAN
and
Geospatial Technologies
for
Next-Generation Smart Cities
Dr M Brindha
Associate Professor
CSE Department
NIT - Trichy
Dr Sekar C
Assistant Professor
School of Computing
SRMIST - Trichy
Presented by:

## Slide 2: Introduction to IoT

## Slide 3
What is IoT?
“The Internet of Things is the network of physical objects that contain embedded technology to communicate and sense or interact with their internal states or the external environment.” Gartner

## Slide 5: IOT MARKET FORECAST
50 Billion
50 Billion
32 Billion
28 Billion
28 Billion
28 Billion
18 Billion
USD 7 Trillion (CAGR: 21%)
USD 1.6 Trillion (CAGR: 13%)
USD 1 Trillion (CAGR: 33%)
“IoT will result in $1.9 trillion in global
economic value-add in 2020” [2013]

## Slide 6: IOT CURRENT APPLICATIONS

## Slide 7: Wireless Technologies
There are many wireless technologies used to connect these devices to the internet
  Short range wireless communication
  Cellular Communication
  LPWAN Communication

## Slide 8: What is LoRa?
PHY Radio Protocol for the Internet of Things
Derivative of Chirp Spread Spectrum
Proprietary to Semtech
Designed for long range, low power; low data rate
Star topology (not mesh or p2p)
Bits to kilobits per second
(depending on channel width & modulation)

## Slide 9: What is LoRaWAN?
Wireless Network for the Internet of Things
  Open, non-proprietary standard
Adds addressing, mobility & localisation
Multiple base stations can receive & process packets
Adaptive data rate scheme to improve performance
Multiple levels of encryption (Network & Application)
Supports time slot scheduling of device transmission

## Slide 10: LoRa Protocol Stack

## Slide 11: LoRaWAN
LoRaWAN™ defines the communication protocol and system architecture for the network while the LoRa® physical layer enables the long-range communication link.
The protocol and network architecture have the most influence in determining the battery lifetime of a node, the network capacity, the quality of service, the security, and the variety of applications served by the network.

## Slide 12: What is LoRaWAN?
LoRaWAN (Long Range Wide Area Network) is a low-power, long-range wireless technology designed for IoT applications.
Derived from Chirp Spread Spectrum (CSS) technology. It encodes information on radio waves using chirp pulses - similar to the way dolphins and bats communicate!
LoRa modulated transmission is robust against disturbances and can be received across Long distances.
Image source : the things network

## Slide 13: What is LoRaWAN?
LoRa is ideal for applications that transmit small chunks of data with low bit rates.
Data can be transmitted at a longer range compared to technologies like WiFi, Bluetooth or ZigBee.
These features make LoRa well suited for sensors and actuators that operate in low power mode.
LoRa can be operated on the license free sub-gigahertz bands, for example, 915 MHz, 868 MHz, and 433 MHz.
It also can be operated on 2.4 GHz to achieve higher data rates compared to sub-gigahertz bands, at the cost of range.
These frequencies fall into ISM bands that are reserved internationally for industrial, scientific, and medical purposes

## Slide 14
Lorawan Network
LoRaWAN
Network
Fully Bi- directional
Standard
Protocol
Secured End- to-End
Easy Commissioning
Built In Mobility
Network
Scalability

## Slide 15
Where Lora Lies
2G
3G
4G
Wi-Fi 11a/b/g/n
Wi-Fi
11ac
Zigbee
RFID
NFC
Data Rate (Mbps)
100
10000
LPWAN
5000
WiMAX
5G
2000
300

## Slide 16
Where Lora Lies

## Slide 17
The most critical factors in a LPWAN are:
Network architecture
Communication range
Battery lifetime or low power
Robustness to interference
Network capacity (maximum number of nodes in a network)
Network security
One-way vs two-way communication
Variety of applications served

## Slide 18: LoRaWAN Features
LoRaWAN is a Media Access Control (MAC) layer protocol built on top of LoRa modulation.
Ultra low power - can last up to 10 years on a single coin cell battery.
Long range - can transmit and receive signals over a distance of over 10 kilometers in rural and up to 3 kilometers in dense urban areas.
Deep indoor penetration - deep indoor coverage, and easily cover multi floor buildings.
License free spectrum - You don’t have to pay expensive frequency spectrum license fees to deploy a LoRaWAN network.
Geolocation- can determine the location of end devices using triangulation without the need for GPS. A LoRa end device can be located if at least three gateways pick up its signal.
End-to-end security- secure communication between the end device and the application server using AES-128 encryption.
Firmware updates over the air - can remotely update firmware (applications and the LoRaWAN stack)

## Slide 19: Battery Lifetime
The nodes in a LoRaWAN™ network are asynchronous and communicate when they have data ready to send whether event-driven or scheduled.
In a mesh network or with a synchronous network, such as cellular, the nodes frequently have to ‘wake up’ to synchronize with the network and check for messages.
This synchronization consumes significant energy and is the number one driver of battery lifetime reduction.
In a recent study and comparison done by GSMA of the various technologies addressing the LPWAN space, LoRaWAN™ showed a 3 to 5 times advantage compared to all other technology options.

## Slide 21: Frequency Band Of Lora Operation

## Slide 22: LoRaWAN: Frequency Bands
EU 433
CN 470-510
CN 779-787
EU 863-870
IN 865-867 (NZ 865-867)
us 902-928
AS 923 (AS 923-925)
AU 915-928

## Slide 23: LoRaWAN Frequency
Image source : 3GLTE info

## Slide 24: Basic Modulation types

## Slide 25: Basic Modulation types

## Slide 26: Basic Modulation types

## Slide 27: Basic Modulation types

## Slide 28: Basic Modulation types

## Slide 29: Basic Modulation types

## Slide 30: Basic Modulation types

## Slide 31: CHIRP SPREAD SPECTRUM
Besides the 3 basic modulation types there are many other modulation types.
• LoRa is a proprietary spread spectrum modulation scheme that is based on Chirp Spread Spectrum modulation (CSS).
• Chirp Spread Spectrum is a spread spectrum technique that uses wideband linear frequency modulated chirp pulses to encode information.
• Spread spectrum techniques are methods by which a signal is deliberately spread in the frequency domain. For example a signal is transmitted in short bursts, "hopping' between frequencies in a pseudo random sequence.

## Slide 32: LoRaWAN Frequency
Image source : 3GLTE info

## Slide 33: Chirps
A chirp, often called a sweep signal, is a tone in which the frequency increases (up-chirp) or decreases (down-chirp) with time.

## Slide 34: LoRA Modulation

## Slide 35: LoRA Modulated Signal
Image source : 3GLTE info

## Slide 36: LoRA Modulated Signal
Image source : 3GLTE info

## Slide 37: LoRA Modulated Signal
Image source : 3GLTE info

## Slide 38: LoRaWAN: Chirp Spread Spectrum
Three Bandwidths Used:
125 KHz
250 KHz
500 KHz
Six Spreading Factors (SF) Used: SF7 - SF12
Each SF step increases air-time by twice

## Slide 39: LoRaWAN Spreading Factors
LoRa Technology: Based on Chirp Spread Spectrum (CSS), where chirps (symbols) carry data.
Spreading Factor (SF):
  Controls chirp rate and data transmission speed.
  Lower SF = faster chirps, higher data rate, but reduced range.
  Higher SF = slower chirps, lower data rate, but increased range.
Range and Data Rate: Adjusting SF balances range and data rate, impacting transmission distance and processing gain.
Congestion Control: Orthogonal SFs prevent interference on the same frequency, allowing multiple transmissions without conflict.
Spreading Factor (SF) and Bit Rate: Lower SF provides a higher bit rate at fixed bandwidth and coding rate. Example: SF7 has a higher bit rate than SF12.
Bandwidth and Bit Rate: Doubling the bandwidth doubles the bit rate for a fixed SF and coding rate.
Example Bit Rates with SF7 and CR = 1:
  125 kHz: 5.5 kbit/s
  250 kHz: 10.9 kbit/s
  500 kHz: 21.9 kbit/s

## Slide 40: LoRaWAN: Spreading Factors

## Slide 41
LoRaWAN: Physical Layer Message
..

## Slide 42
Bitrate
12
11
10
9
14 km
10 km
290 bps
530 bps
970 bps
1,4 sec
Message size of 10 bytes (payload)
0,74 sec
0,37 sec
0,2 sec
8 km 6 km 4 km 2 km
Spreading Factor
8 7 6
2D simulation (flat environment)
Distance between base station and sensor

## Slide 43: LoRaWAN: Data Rates
From Channel Bandwidth * Spreading Factor
Lowest = SF 12 * 125 KHz = 250 bps
Highest = SF 7 * 500 KHz = 21.9 kbps
EU/CN also supports FSK 50 kbps

## Slide 44: Network Capacity
In order to make a long range star network viable, the gateway must have a very high capacity or capability to receive messages from a very high volume of nodes.
The critical factors effecting capacity are the number of concurrent channels, data rate (time on air), the payload length, and how often nodes transmit.
Since LoRa® is a spread spectrum-based modulation, the signals are practically orthogonal to each other when different spreading factors are utilized.
As the spreading factor changes, the effective data rate also changes.
By shifting the data rate higher, the time on air is shortened opening up more potential space for other nodes to transmit.
Adaptive data rate also optimizes the battery lifetime of a node.
In order to make adaptive data rate work, symmetrical up link and down link is required with sufficient downlink capacity.
These features enable a LoRaWAN™ network to have a very high capacity and make the network scalable.

## Slide 45
..
LoRaWAN: Device Classes
..

## Slide 46
Bi-directional end-devices (Class A): End-devices of Class A allow for bi-directional communications whereby each end-device’s uplink transmission is followed by two short downlink receive windows.
This Class A operation is the lowest power end-device system for applications that only require downlink communication from the server shortly after the end-device has sent an uplink transmission.
Class A

## Slide 47: LoRaWAN Device Classes-Class A

## Slide 48: LoRaWAN Device Classes- Class A
All LoRaWAN end-devices must support Class A implementation
Class A devices can send uplink messages at any time.
After an uplink, two short receive windows open for downlink messages.
RX1 Delay and RX2 Delay occur between the uplink and each receive window.
If no response is received in these windows, the next downlink is scheduled after the next uplink.
Class A devices have low power consumption, enabling battery operation.
They spend most time in sleep mode with long intervals between uplinks.
High downlink latency due to needing an uplink before receiving a downlink.

## Slide 49: LoRaWAN Device Classes- Class A
Use Cases
Environmental monitoring
Animal tracking
Forest fire detection
Water leakage detection
Smart parking
Asset tracking
Waste management

## Slide 50
Bi-directional end-devices with scheduled receive slots (Class B): In addition to the Class A random receive windows, Class B devices open extra receive windows at scheduled times.
In order for the end-device to open its receive window at the scheduled time, it receives a time-synchronized beacon from the gateway. This allows the server to know when the end-device is listening.
Class B

## Slide 51: LoRaWAN Device Classes- Class B

## Slide 52: LoRaWAN Device Classes-Class B
Class B Capabilities: Extends Class A by periodically opening receive windows (ping slots) for downlink messages.
Beacons: The network broadcasts time-synchronized beacons, allowing end devices to align their internal clocks for precise timing of downlinks.
Beacon Period: The time interval between two beacons.
Receive Windows: Similar to Class A, RX1 and RX2 open after an uplink.
Latency and Power Consumption:Lower downlink latency than Class A but higher than Class C.
Typically battery-powered; battery life is shorter than Class A due to beacons and ping slots.

## Slide 53: LoRaWAN Device Classes- Class B
Use Cases: Suitable for devices needing medium-criticality downlink timing, such as:
  Utility meters (e.g., electricity, water)
  Street lights
Class A Compatibility: Can also operate in Class A mode if needed.

## Slide 54
Bi-directional end-devices with maximal receive slots (Class C)
End-devices of Class C have almost continuously open receive windows, only closed when transmitting.
Class C

## Slide 55: LoRaWAN Device Classes- Class C

## Slide 56: LoRaWAN Device Classes
Class C
Class C Capabilities: Extends Class A by keeping receive windows open, except during uplink transmissions.
Receive Windows: Opens RX1 and RX2 after uplink, similar to Class A. RX2 remains open continuously until the next uplink.
Low Latency: Can receive downlink messages at almost any time, providing very low latency.
Power Consumption: Higher power usage due to continuous receive windows; typically mains-powered rather than battery-powered.
Use Cases: Ideal for applications needing immediate actuation, such as:
  Utility meters (electric, water)
  Street and beacon lights
  Alarms
Class A Compatibility: Can also switch to Class A mode when needed.

## Slide 57: LoRaWAN Device Classes

## Slide 59: Network Architecture

## Slide 60: LoRaWAN Network Architecture

## Slide 61: LoRaWAN Network Architecture

## Slide 62: LoRaWAN Architecture

## Slide 63: LoRaWAN Architecture
The LoRa Alliance® is an open, non-profit association established in 2015.
LoRaWAN is now an ITU standard
LoRaWAN networks are deployed in a star-of-stars topology.
End Devices - sensors or actuators send LoRa modulated wireless messages to the gateways or receive messages wirelessly back from the gateways. .
Gateways - receive messages from end devices and forward them to the Network Server.
Network Server - a piece of software running on a server that manages the entire network.
Application servers - a piece of software running on a server that is responsible for securely processing application data.

## Slide 64: LoraWAN Entities

## Slide 65: LoRaWAN: End Device
a LoRa client device, sometimes called a mote
  Also sometimes called a node
Communicates with gateways
  And never with other motes or nodes
Has a globally unique identifier called DevEUI
  In the format of an IEEE EUl64 (64 bit)
Has a network unique identifier called DevAddr
  Only network unique 32 bit

## Slide 66: LoRaWAN: End Device

## Slide 67: LoRaWAN: End Device

## Slide 68: LoRaWAN: Gateway
A radio on the infrastructure side
Sometimes called a concentrator or /Jase-station
Communicates with end devices via LoRaWAN
Communicates with a network server via TCP/IP
Can co-exist on multi-protocol base stations
Typically runs a software instance per gateway radio

## Slide 69: LoRaWAN: Gateway

## Slide 70
LoRaWAN: Gateway

## Slide 71: LoRaWAN: Network Server (NS)
The Network Server terminates LoRaWAN MAC layer for End-Devices connected to the network
It is the centre of the star topology
The Network Server decides:
  which Gateway will talk to which End Device
  what data rates will be used by End Devices

## Slide 72
LoRaWAN: Network Server (NS)
THE THINGS
N E T W O R K
I
II I
'I
LOR I 0 T
::ubidots
•••

## Slide 73: LoRaWAN: Join Server (JS)
Server on the Internet Side of a Network Server
Processes join requests from end-devices
End devices cannot be used without joining a network
Often combined with the Network Server

## Slide 74: LoRaWAN: Uplink Message
Communications from end devices to the network server or application
Received via one or more gateways
Uplink Messages received by more than one gateways are de-duplicated by the Network Server

## Slide 75: LoRaWAN: Downlink Message
Communications from network server or application
  via one gateway
  to a single end-device
  or a group of end devices
Network Server decides which gateway is in the best place to send a downlink message to a particular device.

## Slide 76: LoRaWAN: Application
Application layer code running on the end device
Application code running "behind" the network server
Most end devices will run only one application
Identified by a registered IEEE EUl64 value (AppEUI)
"Applications" typically run on Network Servers
  Provide for device management
  Route data to external applications
Misleading name: Could be called application router

## Slide 77: LoRaWAN End Device Activation
Activation Requirement: Every end device must be registered with a network before communication, known as activation.
Activation Methods:
Over-The-Air Activation (OTAA): Most secure and recommended method.Devices perform a join procedure, receiving a dynamic address and negotiating security keys.
Activation By Personalization (ABP): Device address and security keys are hardcoded.Less secure and limits switching between network providers without manual key changes.

## Slide 78: LoRaWAN: Over the Air Join (OTAA)
End devices must have two symmetric keys
Network Session Key (NwkSKey)
Application Key (AppKey)
  Different from the AppSKey
  Unique to every End Device
Device sends DevEUI, AppEUI, and AppKey
Network sends data allowing Dev to derive AppSkey
and NwkSKey (then proceed as a pre-joined device)

## Slide 79: LoRaWAN End Device Activation-OTAA

## Slide 80: LoRaWAN: OTA Join Process
LoRa Device sends JOIN_REOUEST (signed with AppKey). The join request contains the following Information: AppEUI. DevEUI, DevNonce.
DevNonce is a randomly generated number.
The Network Server receives tl1e JOIN_REOUEST and calculates AppSKey and NwkSKey based on: AppKey. AppNonce. NetID and DevNonce.
As with DevNonce, the AppNonce is another randomly generated number.
Network Server generates JOIN_ACCEPT and includes AppNonce
Device receives JOIN_ACCEPT (encrypted with AppKey). The JOIN_ACCEPT contains the following information: AppNonce. Net!D. DevAddr. RFU. RxDely. CFList
Now the Network Server and LoRa device have the same Information and the LoRa device can derive the NwkSkey and AppSKey

## Slide 81: LoRaWAN: OTA Join Process

## Slide 82: LoRaWAN: Pre-Joined Devices (ABP)
End devices must have two symmetric session keys
Devices are personalised with AES 128-bit keys
Network Session Key (NwkSKey)
  Known only by the network operator
  Protects network metadata
Application Session Key (AppSKey)
  Common to all End Devices using an Application
  Known only to the Application Operator

## Slide 83: LoRaWAN End Device Activation

## Slide 84: Security
It is extremely important for any LPWAN to incorporate security.
LoRaWAN™ utilizes two layers of security: one for the network and one for the application.
The network security ensures authenticity of the node in the network while the application layer of security ensures the network operator does not have access to the end user’s application data.
AES encryption is used.

## Slide 85: Is LoRaWAN secure? How are the LoRaWAN protocol networks secured?
LoRaWAN Security

## Slide 86: LoRaWAN: Encryption
All payloads are encrypted
No possibility for attackers to read payloads
No possibility for network operator to read payloads
and have data integrity
No possibility for changing data in flight
No possibility for intercepting & replaying data
MAC commands are protected (except frame options)
No possibility for attackers to read metadata

## Slide 87
General Wireless Security

## Slide 88
Confidentiality is probably the most common aspect of information security. We need to protect our confidential information. An organization needs to guard against those malicious actions that endanger the confidentiality of its information.
Confidentiality

## Slide 89
Integrity
Information needs to be changed constantly. Integrity means that changes need to be done only by authorized entities and through authorized mechanisms.

## Slide 90
Availability
The information created and stored by an organization needs to be available to authorized entities. Information needs to be constantly changed, which means it must be accessible to authorized entities.

## Slide 91
1.91
Taxonomy of attacks with relation to security goals
Notes: 1.#

## Slide 92
Attacks Threatening Confidentiality
Snooping refers to unauthorized access to or interception of data.
Traffic analysis refers to obtaining some other type of information by monitoring online traffic.
Notes: 1.#

## Slide 93
Attacks Threatening Integrity
Modification means that the attacker intercepts the message and changes it.
Masquerading or spoofing happens when the attacker impersonates somebody else.
Replaying means the attacker obtains a copy of a message sent by a user and later tries to replay it.
Repudiation means that sender of the message might later deny that she has sent the message; the receiver of the message might later deny that he has received the message.
Notes: 1.#

## Slide 94
Attacks Threatening Availability
Denial of service (DoS) is a very common attack. It may slow down or totally interrupt the service of a system.
Notes: 1.#

## Slide 95: Security Attack Classification

## Slide 96: Symmetric Key Cryptography
How to send this Key?
Ref Book:Cryptography and Network Security by Forouzan

## Slide 97: Secret Key Cryptography
Also called symmetric or single‐key algorithms.
The encryption and the decryption key are the same.
Techniques based on a combination of substitution and permutation.
Stream ciphers: operate on single bit or byte.
Block ciphers: operate on blocks (typically 64/128/256… bits)
Advantage: simple, fast.
Disadvantage: key exchange, key management.
Examples: DES,RC4, IDEA, Blowfish, AES, etc.

## Slide 98
Message Integrity
The cryptography systems that we have studied so far provide secrecy, or confidentiality, but not integrity.
However, there are occasions where we may not even need secrecy but instead must have integrity.
For example, Alice may write a will to distribute her estate upon her death.
The will does not need to be encrypted.
After her death, anyone can examine the will.
The integrity of the will, however, needs to be preserved.
Alice does not want the contents of the will to be changed.

## Slide 99
Message and digest

## Slide 100
Mutual End Point Authentication

## Slide 101
Mutual End Point Authentication

## Slide 102
Session Key Generation and Delivery

## Slide 103
Data Origin Authentication, Integrity and Replay Protection

## Slide 104
Payload Encryption +Data Origin Authentication, Integrity/Replay Protection

## Slide 105
LoRa WAN End-to-End (Transport) Security

## Slide 106
LoRa WAN End-to-End (Transport) Security

## Slide 107
Overall/ Complete Security

## Slide 108
OTAA Vs ABP

## Slide 109: LoRaWAN Security
Security Keys : NwkSKey, AppSKey and AppKey
When a device joins the network (this is called a join or activation), an application session key AppSKey and a network session key NwkSKey are generated. The NwkSKey is shared with the network, while the AppSKey is kept private. These session keys will be used for the duration of the session.
The AppSKey is used for encryption and decryption of the payload.
The application key (AppKey) is only known by the device and by the application.

## Slide 110: Hardware

## Slide 111: Dashboard

## Slide 112
LoRaWAN Ecosystem : Modules

## Slide 113
LoRaWAN Ecosystem : Things

## Slide 114
LoRaWA N Ecosystem : Gateways

## Slide 115: LoRaWAN: Network Servers
Actility: https://www.actility.com/
Cable Labs: https://www.loraserver.io/
EveryNet: http://everynet.com/
Loriot: https://loriot.io/
ResloT: https://www.resiot.io/en/
The Things Network: https:// www.thethingsnetwork.org/

## Slide 116
LoRaWAN: Application Platforms

## Slide 117: LoRaWAN: Selected Platforms
Actility ThingPark
Amazon AWS loT
EveryNet
IBM BlueMix
Microsoft Azure loT
MyDevices Cayenne
OpenChirp
Stream loTx

## Slide 118: LoRaWAN Limitations
  Not suitable for:
    Real-time data: Limited to small, infrequent packets.
    Phone calls: Use GPRS/3G/LTE instead.
    Home automation: Use ZigBee or Bluetooth.
    High-data tasks: For photos or video, use WiFi.
Uplink Efficiency Tips:
  Payload: Minimize size; use binary format (e.g., Cayenne LPP).
  Message Interval: Send at several-minute intervals or upon significant changes.
  Data Rate: Start with SF7BW125 for low power and airtime; enable Adaptive Data Rate (ADR) if needed.
Downlink Efficiency Tips:
  Minimize Downlinks: Avoid if possible, use small payloads.
  Data Rate: Downlink rate depends on uplink efficiency.
  Avoid Confirmations: Use unconfirmed uplinks if possible to reduce network load and boost reliability.

## Slide 119
What is a Smart City?
It’s a city outfitted with high-tech communication capabilities.
It uses digital technology to enhance performance and well being, to reduce costs and resource consumption, and to engage more effectively and actively with its citizens.
Prime Minister Narendra Modi’s vision ‘Digital India’, has a plan to build 100 smart cities across the country.
Modi in his speech said, “Cities in the past were built on riverbanks. They are now built along highways. But in the future, they will be built based on availability of optical fiber networks and next-generation infrastructure.”

## Slide 121
Why smart city ???

## Slide 122: IoT and Smart Cities
Smart cities aim to improve quality of life, sustainability, and efficiency, addressing urban challenges like congestion, pollution, and resource management.
IoT (Internet of Things): Connects devices across urban environments, collecting real-time data for monitoring and control.’
LoRaWAN (Long Range Wide Area Network): Provides low-power, long-distance communication ideal for large-scale IoT networks in cities.
GIS (Geographical Information Systems): Visualizes spatial data, enabling urban planners to make data-driven decisions.
GPS (Global Positioning System): Supports tracking of assets and optimizing public services like transportation.

## Slide 123: LoRaWAN Usecase
Image source : Semtech

## Slide 124: Jamshedpur – A Smart City
Successful Initiatives
Smart Bins
Smart Parking
Smart Lighting
Smart Manholes
Water Tank Level Detector
Smart Pond Management System
Intrusion Detectors
Smart Transformer Monitoring System

## Slide 125: Smart Bins
Smart bins have been installed in Jamshedpur which senses if the dustbin is filled up or not and sends the data through Lora.

## Slide 126
Smart Bins with Sensors installed in Jamshedpur

## Slide 127: Smart Parking
Parking Sensors senses if there is a vehicles present in the parking spot or not and thereby, sends an appropriate signal through Lora.
This data is used to know where parking spaces are empty and thus help the traffic in parking their vehicles.

## Slide 128
Parking Sensors placed in Jamshedpur

## Slide 129: Smart Lighting
Street Lights integrated with Lora modules are put across streets in Jamshedpur which help in controlling their working from one control station.
This helps in saving a lot of power as the street lights are switched on and switched off in time and lights are dimmed at nights .

## Slide 130
A Street light in Jamshedpur .

## Slide 131: Smart Manholes
Manholes are fitted with sensors which help them know the level of water in the manhole and thus help in controlling overflow.

## Slide 132: Manholes installed with sensors fitted with lora modules in Jamshedpur.

## Slide 133: Water Tank Level Detector
Water Tank Level Detectors are installed across water tanks in Jamshedpur which help in knowing the real time water level in tanks in the control room

## Slide 134: Water tank level sensor installed in Kadma, jamshedpur.

## Slide 135: Smart Pond Management System
Smart Pond Management Sensors are put in different ponds to help in knowing the DO, amount of chlorine in the water at any given time to help the aquatic life flourish.

## Slide 136: Intrusion Detectors
Intrusion Detectors are installed in places where high security is needed like the water tank distribution area.

## Slide 137: Smart Transformer Monitoring System
Lora modules help the sensors put inside the transformers to send the temperature readings and thereby, help in monitoring the condition of the transformer and ensure timely repairs.

## Slide 138: Integration of LoRaWAN and Geospatial Technologies
Real-Time Data Collection with LoRaWAN Sensors
Key Benefits:
  Wide Coverage: Ideal for urban environments, covering large areas with fewer gateways.
  Low Power Consumption: Extends the battery life of sensors, making them suitable for continuous monitoring.
  Real-Time Data: Provides timely data on various urban metrics, such as:
    Air quality levels
    Noise pollution
    Traffic flow
    Waste management metrics
  Scalability: Easily integrates additional sensors as urban needs grow

## Slide 139: Integration of LoRaWAN and Geospatial Technologies
Geospatial Platforms (GIS)
Role of GIS in Urban Management: Geographic Information Systems (GIS) facilitate the analysis, visualization, and management of spatial data.
Visualization of Data:
  Map-Based Interfaces: Present data collected from LoRaWAN sensors in an easily interpretable format.
  Layered Data Analysis: Users can overlay multiple datasets (e.g., traffic, air quality) to identify patterns and correlations.
Enhanced Decision-Making:
  Informed Urban Planning: Leverages real-time data to make proactive decisions regarding infrastructure and services.
  Responsive Policy Formulation: Data-driven insights enable local governments to address urban challenges effectively.
Image source : Geospatial World

## Slide 140: The Things Industries is a full-service LoRaWAN solutions provider
Image source : the things network
Build, grow and scale with The Things Stack Cloud

## Slide 141
Thank You!!!